## Slide 1: Constraining VOC emission from western US wildfires with WE-CAN and FIREX-AQ airborne observations
Lixu Jin, Wade Permar, WE-CAN team, FIREX-AQ team, and Lu Hu
University of Montana
  Email: lixu.jin@umconnect.umt.edu

## Slide 2
The total VOC emissions diff by 30-40% across 3 widely used BB emission inventories for this region (GFED4, QFED, and GFAS).
In the 2019 fire season, the VOC BB emission is only 1/6 of that in 2018 for this region.
405 GgC or 14%
2272 GgC or 78%
[1e12 atomsC/cm2/s]
Biomass burning/Anthropogenic
Biogenic
242 GgC or 8%
Biomass burning (GFAS)
Anthropogenic (EPA NEI 2011)
Biogenic (MEGAN)
Current understanding of primary VOC emission in 2018 Summer

## Slide 3
The total VOC emissions diff by 30-40% across 3 widely used BB emission inventories for this region (GFED4, QFED, and GFAS).
In the 2019 fire season, the VOC BB emission is only 1/6 of that in 2018 for this region.
405 GgC or 14%
2272 GgC or 78%
[1e12 atomsC/cm2/s]
Biomass burning/Anthropogenic
Biogenic
242 GgC or 8%
Biomass burning (GFAS)
Anthropogenic (EPA NEI 2011)
Biogenic (MEGAN)
Current understanding of primary VOC emission in 2018 Summer
GEOS-Chem suggests that biomass burning (BB) only account for <10% of the primary VOC emission in the western US. Is it true?

## Slide 4
Mod vs mod: GEOS-Chem + GFAS tends to reproduce higher and better VOCs mixing ratios.
Mod vs obs: GEOS-Chem with different inventories can reproduce the BB enhancements in the campaign averaged profiles but systematically underpredict observed VOC abundance by a factor of 2-6.
Question: Is the negative bias from BB emissions? How much and why?
C-130 observation
GEOS-Chem + GFED4
GEOS-Chem + GFAS
GEOS-Chem + QFED
GEOS-Chem + noBB
VOC vertical profiles over western US (WE-CAN)
Analysis is conducted for other 11 VOCs (not shown here)

## Slide 5
C-130 observation
GEOS-Chem + GFED4
GEOS-Chem + GFAS
GEOS-Chem + QFED
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB
Question: Why does model underpredict BB emission?
C-130 observation
GEOS-Chem + GFED4
GEOS-Chem + GFAS
GEOS-Chem + QFED
GEOS-Chem + noBB
GEOS-Chem + 3 × GFAS
VOC vertical profiles over western US (WE-CAN)
The best-case simulation (GEOS-Chem + GFAS) underestimates the BB emission by a factor of 3-5.
For primary VOCs, tripling BB emissions agree the WE-CAN observation within measurement uncertainty; For OVOCs, there are likely missing photochemical production sources in the model.

## Slide 6
GFAS is selected for BB emission in this sensitivity test.
The GEOS-Chem + Injection experiments tend to agree within 10%, suggesting that GEOS-Chem is not sensitive to those assumptions of how BB emissions are released vertically (at least for observation we used).
Data credit:
Jeff Pierce (Bop2top)
VOC vertical profiles over western US (WE-CAN)
Injection height

## Slide 7
VOC vs CO emission ratio (WE-CAN)
Emission ratio test: the best representation (GFAS) tends to agree observed ER within ± 30 %.
Fire detection experiment suggests the all 3 inventories can detect ~ 30 fires we sampled during WE-CAN.
=> VOC emission ratio and fire detection are not significant model errors in the GEOS-Chem.
VOC vs CO emission ratio (WE-CAN)
Similar analysis is conducted for FIREX-AQ and the conclusions hold.
Injection height
Emission ratio
Fire detection

## Slide 8
VOC vs CO emission ratio (WE-CAN)
How does BB emission inventory work?
  Simple math: Emission estimates (g) = Emission factor (g/kg dry matter burnt) × dry matter burnt (kg)
  Emission ratio and emission factor both suggest similar information.
=> The BB underestimation is driven the underestimation of dry matter burnt.
VOC vs CO emission ratio (WE-CAN)
Similar analysis is conducted for FIREX-AQ and the conclusions hold.
Question: Can the BB underestimation be applied to the widespread western US?
Injection height
Emission ratio
Fire detection
Dry matter burnt
Notes: Lhu, need to explain why the dry matter burnt is wrong: i.e., low obit satellites doesn’t have enough temporal and spatial resolutions, cloud interferences etc.

## Slide 9
Data credit:
Dan Jaffe (Mt Bachelor), Bob Yokelson and Vanessa Selimovic (Missoula), and EPA (rest)
CO mixing ratios time series (WE-CAN)
The base model (GEOS-Chem + GFAS) does underestimate BB emissions across western US.
The 3 × GFAS simulation systematically improves the model mean bias across western US for 7 fire-influenced sites without degrading correlation coefficients with observations.
These ground measurements also point to the BB emission underestimation across western US.
Observation
GEOS-Chem + GFAS (base)
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB
Observation
GEOS-Chem + GFAS (base)
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB

## Slide 10
A significant amount reactive carbon from wildfire is missing in the GEOS-Chem
  Emission: VOC emission from wildfire can account for 30-60% of the total primary VOC emission (1-8% of total before), considering the dry matter burnt underestimation and unmodeled VOCs.
  Chemistry: Among top 10 OH reactivity contributor, 4 of them are not included in the GEOS-Chem: three of them are furans (furan and its derivatives) and the remaining one is butadiene.
< 20 BB VOCs
161 BB VOCs
Thanks Tess for providing a nice background about furans!

## Slide 11
Summary
Conclusions:
  Three commonly-used BB inventories underestimate the BB emissions due to underprediction of dry matter burnt in the western US.
  Tripling the BB emission (3 × GFAS) systematically improves model: observation comparisons for primary VOCs. However, the model misses photochemical production sources for OVOCs.
  BB emissions play a far more important role than previous understanding.
  To be submitted. Stay tuned!
  lixu.jin@umconnect.umt.edu
  Twitter: @Lixu_Jin
Future work:
  GEOS-Chem chemistry mechanisms miss secondary HCHO production source by comparing to near-explicit chemistry (MCM).
  We need to figure out the missing secondary source for formaldehyde.
  Also , we will customize chemistry of furans and other VOCs into the GEOS-Chem, due to their significant OH reactivity contribution and corresponding chemical impacts.
Observation
GEOS-Chem chemical mechanism
Explicit chemical mechanism (MCM)

## Slide 12: Additional materials (see following slides)

## Slide 13
VOC vs CO emission ratio

## Slide 14
Simple math is conducted to derive the underpredicted BB:
BB impacts = full datasets – least fire conditions
Underestimated BB impacts = BB impacts from observation – from model
Model underestimates by a factor of 3-5 for primary trace gases (similar conclusion is gained for the 2019 FIRE-AQ)
Tripling the BB emissions in the model agree observed VOCs within observation uncertainty except xylenes and OVOCs (formaldehyde here).
Why are BB emissions underestimated?
(e.g., emission factors, fuel burned, fire detections, and injections?)
The model underpredicts the BB emissions by a factor of 3-5 (Q1 and Q2)

## Slide 15
C-130 observations
GEOS-Chem + Bop2top
GEOS-Chem + MAMI
GEOS-Chem + PBL65_FT35
GEOS-Chem + Sf2mami
GEOS-Chem + Surface
VOCs vertical profiles over the western US (FIREX-AQ)
DC-8 observations
GEOS-Chem + GFAS
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB
Mixing ratio (ppb)
Pressure(hPa)
Similar conclusion supported by FIREX-AQ: GEOS-Chem + GFAS can reproduce the BB enhancements in the profile but systematically underpredict BB-related source by a factor of 3-6 for primary VOCs (except MEK; a factor of 2-5 in the WE-CAN).
Formaldehyde
Acetaldehyde
Acetone
MEK
Benzene
Toluene
Xylenes
Propane

## Slide 16
PTR-ToF-MS observation
TOGA observation
I-CIMS observation
GEOS-Chem + GFED4
GEOS-Chem + GFAS
GEOS-Chem + QFED
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB
Formic acid
Acetic acid
Lumped C ≥ 3 aldehydes
VOC vertical profiles over western US (WE-CAN)
Missing photochemical production source for formic acid, acetic acid, and lumped C ≥ 3 aldehyde

## Slide 17
Mixing ratio (ppb)
Pressure(hPa)
C-130 observations
TOGA observation
GEOS-Chem + GFED4
GEOS-Chem + GFAS
GEOS-Chem + QFED
Formaldehyde
Acetaldehyde
Acetone
MEK
Benzene
Toluene
Xylenes
Propane
VOC vertical profiles over western US (least-fires region for WE-CAN)

## Slide 18
VOCs vertical profiles over the western US (least BB-impacted for FIREX-AQ)
DC-8 observations
GEOS-Chem + GFAS
GEOS-Chem + 3 × GFAS
GEOS-Chem + noBB
Mixing ratio (ppb)
Pressure(hPa)
Formaldehyde
Acetaldehyde
Acetone
MEK
Benzene
Toluene
Xylenes
Propane
There are problems beyond BB emissions as suggested by the relatively clean environment: missing HCHO, acetaldehyde, propane, benzene, and toluene.